## Slide 1
學期實驗大綱
FCDNN design & its software implementation – 9/25
MIPS assembly programming – 10/9
FC-DNN implementation on Zynq – 10/16
Hardware modeling (Verilog), simulation, & implementation – 10/23
Tiny MIPS as an accelerator (software, hardware) – 11/20、11/25
Trace-driven cache simulation – 12/11

## Slide 2
Advisor: Tay-Jyi Lin
助教: 郭立揚
MIPS assembly programming

## Slide 3
實驗目的
  熟悉Mars IDE，並利用MIPS組合語言撰寫出簡單遞迴小程式
  觀察程式執行時，暫存器之數值變化

## Slide 4
Outline
MIPS overview
  Register definition
  Instruction format
  Basic instructions
Mars IDE usage
Useful system call (MARS)
Example & Exercise
Homework

## Slide 5
Outline
MIPS overview
  Register definition
  Instruction format
  Basic instructions
Mars IDE usage
Useful system call (MARS)
Example & Exercise
Homework

## Slide 6
MIPS overview – Register definition
 | Type | Name | Number | Comments
GPR | Assembler related | $at | $1 | Reserved for assembler
 | OS related | $k0, $k1 | $26, $27 | Reserved for interrupt the trap handlers (OS)
 | Procedure call | $v0, $v1 | $2, $3 | Registers used for function calls and return values
 |  | $a0, ..., $a3 | $4, ..., $7 | First four arguments to functions. EX: add(int a0, int a1);
 |  | $ra | $31 | Return address
 | Variables/constant | $s0, ..., $s7 | $16, ..., $23 | Saved registers
 |  | $t0, ..., $t7 | $8, ..., $15 | Temporary registers
 |  | $t8, $t9 | $24, $25 | More temporary registers
 |  | $zero, $r0 | $0 | Always zero
 | Memory mangement | $gp | $28 | Global pointer (static data)
 |  | $sp | $29 | Stack pointer
 |  | $fp | $30 | Frame pointer

## Slide 7
MIPS overview – Instruction format
  指令格式:
  R type:
    用途：算術運算和邏輯操作
    指令：add, sub, and, srl, sll…
  I type:
    用途：Load/Store、branch、立即值操作
    指令：lw, sw, beq, bne, addi…
  J type:
    用途：跳轉操作
    指令：j, jal…

## Slide 8
MIPS overview – Basic instructions
Mnemonic | Syntax |  | Operation
LW | lw | $t, offset($s) | $t=MEM[$s+offset]
SW | sw | $t, offset($s) | MEM[$s+offset] =$t
ADD | add | $d, $s, $t | $d =$s + $t
ADDU | addu | $d, $s, $t | $d =$s + $t
SUB | sub | $d, $s, $t | $d =$s - $t
SUBU | subu | $d, $s, $t | $d =$s - $t
AND | and | $d, $s, $t | $d =$s & $t
OR | or | $d, $s, $t | $d =$s ¦ $t
XOR | xor | $d, $s, $t | $d =$s ^ $t
NOR | nor | $d, $s, $t | $d = ~($s ¦ $t)
SLL | sll | $d, $t, shamt | $d =$s << shamt
SRL | srl | $d, $t, shamt | $d =$s >> shamt
SRA | sra | $d, $t, shamt | $d =$s >> shamt
BEQ | beq | $s, $t, offset | if $s==$t advance_pc
BNE | bne | $s, $t, offset | if $s!=$t advance_pc
J | j | target | pc=pc&(000000 ¦ target)

## Slide 9
Outline
MIPS overview
  Register definition
  Instruction format
  Basic instructions
Mars IDE usage
Useful system call (MARS)
Example & Exercise
Homework

## Slide 10
工具列
編輯區
標準輸入與標準輸出
暫存器訊息
MARS IDE Usage – UI介紹

## Slide 11
開啟舊檔
MARS IDE Usage – 匯入檔案與執行

## Slide 12
選取檔案
MARS IDE Usage – 匯入檔案

## Slide 13
組譯
執行一條指令
指令檢視
資料檢視
暫存器檢視
MARS IDE Usage – 組譯與執行

## Slide 14
點擊help
基本指令
系統呼叫
MARS IDE Usage – 指令集

## Slide 15
MARS IDE Usage – 指令執行次數

## Slide 16
Outline
MIPS overview
  Register definition
  Instruction format
  Basic instructions
Mars IDE usage
Useful system call (MARS)
Example & Exercise
Homework

## Slide 17
Service | Code in $v0 | Arguments | Result
print integer | 1 | $a0 = integer to print | 
print float | 2 | $f12 = float to print | 
print double | 3 | $f12 = double to print | 
print string | 4 | $a0 = address of null-terminated string to print | 
read integer | 5 |  | Read $v0 (integer)
read float | 6 |  | Read $f0 (float)
read double | 7 |  | Read $f0 (double)
Useful system call (MARS)

## Slide 18
Outline
MIPS overview
  Register definition
  Instruction format
  Basic instructions
Mars IDE usage
Useful system call (MARS)
Example & Exercise
Homework

## Slide 19
.data
inputa:.asciiz "Enter factorial number="
.text
.globl main
main:
li $v0,4
la $a0,inputa
syscall
li $v0,5
syscall
add $a0, $zero, $v0
jal fact
add $t1, $zero, $v0
li $v0,1
add $a0, $zero, $t1
syscall
j exit
fact:
addi $sp, $sp, -8
sw $ra, 0($sp)
sw $a0, 4($sp)
slti $t0, $a0, 1
beq $t0, $zero, L1
addi $v0, $zero, 1
addi $sp, $sp, 8
jr $ra
L1:
addi $a0, $a0, -1
jal fact
lw $a0, 4($sp)
mul $v0, $a0, $v0
lw $ra, 0($sp)
addi, $sp, $sp, 8
jr $ra
exit:
  階乘範例:
    遞迴關係式:
印出inputa
接收keyboard input
印出運算結果
保存遞迴的資訊
判斷是否為
最後一筆
將n減1，跳回
原本函數
乘法運算
Example - 階乘

## Slide 20
  課堂練習
    執行範例程式，輸入欲計算之階乘數
    輸入兩自然數，相減後輸出結果
      程式運行範例：
          Enter num1 = 70
          Enter num2 = 50
          Ans = 20
Exercise

## Slide 21
Outline
MIPS overview
  Register definition
  Instruction format
  Basic instructions
Mars IDE usage
Useful system call (MARS)
Example & Exercise
Homework

## Slide 22
  作業內容：
    作業目標：
      透過簡單的FC-DNN C code編寫組合語言，並和C code比較答案是否一致
    流程：
      透過提供的FC-DNN C code撰寫組合語言
      在Mars執行自行撰寫好的.asm
      神經元輸出觀察
      比較與FC-DNN C code答案是否相同
    神經元比較範例 (請務必按照C code中所提供的權重)：
        dnn_golden_ans.c編譯與執行：
        編譯：LAB2/homework $ gcc dnn_golden_ans.c –o dnn_golden_ans
        執行：LAB2/homework $ ./dnn_golden_ans
        bed6e68b (將輸出結果與Mars做比對)
        組語Output神經元觀察：
          根據儲存的記憶體位址進行比較
Homework
x1
x2
x3
x4
h1
h2
y1
code架構(4、2、1)

## Slide 23
  繳交內容：
    組合語言設計檔 (.asm檔)
    組合語言神經元輸出結果，請用紅框標出 (screen shot)
    指令執行次數 (screen shot)
  上傳格式：
    將檔案壓縮為.zip壓縮檔上傳
    壓縮檔檔名以(學號_姓名_lab2.zip)為命名
  評分標準：
    完成課堂練習(40%)
    回家作業(60%)
      功能設計正確(40%)
      指令執行次數(20%)
          1 ~ 10 名 20%
          10 ~ 20 名 10%
          21 ~ 名 0%
Homework

## Slide 24
  繳交期限：
    2023/10/15 23:59前上傳ecourse2
  注意：
    遲交、未交者不予計分。(遲交者在期末保有調分機會)
Homework

## Slide 25: Appendix

## Slide 26
  Java：
    https://www.java.com/en/download/
  Mars：
    http://courses.missouristate.edu/kenvollmar/mars/
環境建置

## Slide 27
安裝win10 gcc編譯環境 – 安裝mingw

## Slide 28
安裝win10 gcc編譯環境 – 安裝mingw

## Slide 29
安裝win10 gcc編譯環境 – 安裝mingw

## Slide 30
安裝win10 gcc編譯環境 – 環境變數設定
3. 點擊 進階系統設定
對windows點右鍵
選取 系統

## Slide 31
安裝win10 gcc編譯環境 – 環境變數設定
4. 點擊環境變數
5. 點擊path並按下編輯
6. 新增並輸入bin資料夾路徑，
按下確定。
C:\MinGW\bin